## Slide 1: ECE 278
Hardware version of ORCs machine

## Slide 2: Summary of our machine
Machine word size = 16 bits
Registers = $PC, $SR, $0, $1, …, $15, $IR1, $IR2
  $15 reserved for addresses, but can be accessed…very volatile
Register instructions =
  0000 - MOVE R1, R2 R1 <- R2
  0001 - MOVEI R1, <Constant> R1 <- <constant>
Memory instructions =
  0100 - LOAD R1, <Address> R1 <- Memory[Address]
  0101 - STORE R1, <Address> Memory[Address] <- R1
  0110 - LOADR R1, R2 R1 <- Memory[R2]
  0111 - STORER R1, R2 Memory[R2] <- R1
ALU instructions =
  1000 - ADD R1, R2 R1 <- R1 + R2
  1001 - SUB R1, R2 R1 <- R1 – R2
Control instructions =
  1100 - JMPNEG <Address> if (last operation == -’ve) PC <- Address
  1101 - JMPZ <Address> if (last operation == zero) PC <- Address
  1110 - JMP <Address> PC <- Address

## Slide 3: Figure 1

## Slide 4: Machine Instructions
4-bits for operation
4-bits for registers
16 bit instruction with 4 useless bits
Op R1, R2 = {4’b0000, R2, R1, Op}
  Add $5, $6 = 0x0658
    6 = $6, 5 = $5, 8 = Add
Instructions with constants are 32 bits = 16 bits for Instruction, and 16 bit for Constant
  MoveI, Load, Store, JMP, JMPNEG, JMPZ

## Slide 5: Memory
Only word access
Addresses are in increments of 16bits, therefore 0x0 and 0x1 are addresses of words
Memory is a multi clock access due to registers in Altera memory instantiation

## Slide 6: Program 1
0x0 - Movei $0, 0x5 0x0001, 0x0005 – 1, 5
0x2 - Movei $1, 0x1 0x0011, 0x0001 – 17, 1
0x4 - Move $2, $1 0x0120 - 288
0x5 - Add $1, $0 0x0018 - 24
0x6 - Sub $0, $2 0x0209 - 521
0x7 - JMPZ 0xb 0x000d, 0x000b – 13, 11
0x9 - JMP 0x5 0x000e, 0x0000 – 14, 5
0xb - END 0x000f - 15

## Slide 7: Program 2
0x0 - Movei $0, 0x5 0x0001, 0x0005 – 1, 5
0x2 - Movei $1, 0x1 0x0011, 0x0001 – 17, 1
0x4 - Movei $2, 0x200 0x0021, 0x0200 – 33, 512
0x6 - Movei $3, 0x100 0x0031, 0x0100 – 49, 256
0x8 - Store $0, 0x100 0x0005, 0x0100 – 5, 256
0xa - StoreR $1, $2 0x0217 - 535
0xb - LoadR $4, $3 0x0346 – 838
0xc - Load $5, 0x200 0x0054, 0x0200 – 84, 512
0xe - END 0x000f - 15